## Slide 1: Addressing modes

## Slide 2
Addressing modes:The way of specifying data to be operated by an instruction is known as addressing modes.
(or)
The way for which an operand is specified for an instruction in the accumulator, in a general purpose register or in memory location, is called addressing mode.
There are 8 different addressing modes:
1)Immediate addressing mode
2)Register addressing mode
3)Direct addressing mode
4)Register indirect addressing mode
5)Based addressing mode
6)Indexed addressing mode
7)Based indexed addressing mode
8)Based index with displacement mode

## Slide 3
1)Immediate Addressing: In immediate addressing, the operand is specified in the instruction itself.
Examples:
MOV AL, 35H
MOV BX, 0301H
ADD AX, 4836H
2) Register Addressing: In register addressing, the operand is placed in one of the 16-bit or 8-bit general purpose registers.
Examples:
MOV CX, AX (Copies content of 16 bit AX register into 16 bit CX register)
ADD AL, BL
ADD CX, DX

## Slide 4
3)Direct addressing mode:The addressing mode in which the effective address of the memory location is written directly in the instruction.
Examples: MOV AX, [1592H]
MOV AL, [0300H]
4)Register indirect addressing mode: This addressing mode allows data to be addressed at any memory location through an offset address held in any of the following registers: BP, BX, DI & SI.
Example:MOV AX, [BX] ; Suppose the register BX contains 4895H, then the contents ; 4895H are moved to AX
5)Based addressing mode: In this addressing mode, the offset address of the operand is given by the sum of contents of the BX/BP registers and 8-bit/16-bit displacement.
Example: MOV DX, [BX+04]
ADD CL, [BX+08]

## Slide 5
6)Indexed addressing mode: In this addressing mode, the operands offset address is found by adding the contents of SI or DI register and 8-bit/16-bit displacements.
Examples: MOV BX, [SI+16]
ADD AL, [DI+16]
7) Based-index addressing mode: In this addressing mode, the offset address of the operand is computed by summing the base register to the contents of an Index register.
Example: ADD CX, [BX+SI]
MOV AX, [BX+DI]
8) Based indexed with displacement mode: In this addressing mode, the operands offset is computed by adding the base register contents. An Index registers contents and 8 or 16-bit displacement
Example:MOV AX, [BX+DI+08],
ADD CX, [BX+SI+16]